## Slide 1: Embedded Cryptography and Side-Channel Analysis From past to present … and beyond …
Benoît Feix
STMicroelectronics
Cryptis Master2, October 2024.

## Slide 2: Agenda
1
Hardware attacks
2
Side-channel is coming
3
A taste of RSA
4
Side-channel methodology
5
Post Quantum Cryptography
6
Resources, nowadays
7
Attack potential and standards

## Slide 3: Agenda
Past: from 90’s ... Before Kocher ..
Designing a security product
Invasive Attacks and Countermeasures
96’s: (well?)coming side-channel attacks
Simple Analysis, explanations, demos
Differential Analysis, DPA, CPA, demos on DES and AES
Countermeasures, High Order on Symmetric Algorithm and CMs: demo
Back to RSA
Differential Analysis: demo
Countermeasures
Side-channel Methodology
Demos on t test and reverse analysis
Nowadays
No more ‘confidential’ science, open sources and CTF
Recent attacks
Post Quantum Cryptography
Standard and attack ratings in the industry

## Slide 4: Secure Products Invasive Attacks and Countermeasures

## Slide 5: Started with smart cards …

## Slide 6: Integrated Circuit Architecture
Processor:
  8, 16 or 32 bits
  CISC or RISC
  Harvard or Von Neumann
ROM: Read Only Memory
RAM: Random Access Memory
EEPROM: Electrically Erasable Programmable Read Only Memory
Flash: NOR or NAND – close to EEPROM
RNG: Random Number Generator
Coprocessors for:
  TDES, AES
  CRC, HASH
  Long Integer Arithmetic (RSA, ECDH, ECDSA)
In/Out IPs
MPU/MMU: Memory Management Unit
Security sensors

## Slide 7: Product Conception Phases
OS
Développement
Circuit Intégré
Développement
CRYPTO
Développement
Applications
Développement
Sécurisation
Tests
Production
Préparation
Fabrication
Photomasks
Fonderie
Tests
Initialisation
Pré
personnalisation
Produit
Pré
personnalisation
Personnalisation

## Slide 8: Different Phases From User to End-Of-Life cycles
  - Désactivation,
  - Usure fonctionnelle
  - Casse
Mise en circulation
    - Traitement des commandes
    - Mises à jour (modifications données)
Gestion du Parc
    - Remplacements
    - Vols, oppositions, pertes
Fin de vie

## Slide 9: Standard Crypto Algorithms in Products
Symmetric
  DES/TDES: NIST recommendation now TDES EDE3 for 240 use of same key
  AES 128-192-256
  SM4, SEED, FEAL-32
Hash Functions
  SHA-1, SHA-256
  RIPEMD 160
  SHA-3: KECCAK
  HMAC Functions
  SM3
Asymmetric
  CRT-RSA – RSA SFM (≥ 2048 bit)
  DSA / ECDSA (i.e. GF-P256)
  DH / ECDH
  OBKG, Kgen
  SM2
And also …
DRBG, example: AES-CTR based i.e. NIST SP800-90
Stream Ciphers
Lightweight crypto
Post Quantum Cryptography

## Slide 10: Reverse Engineering
Accessing to the circuit
  Remove plastic or open with a knife or cutter
  Use chemical products to remove (destroy) epoxy (resin) with nitric acid and acetone …
    We observe now the chip that we can analyze using microscope(s)
    Reconnect the circuit on another ‘’package’’
      In order to use it again we reconnect the IO pins, clock pins, VCC pads, etc.
  We can then analyze the IC when running with several tools

## Slide 11: Reverse Engineering Reverse the IC Layout
Re-assemble metal layers
  Integrated Circuit = SUM of metal layers interconnected each others
  Using an optical microscope we can observe and take a picture of each metal layer
    We start at the higher (upper) layer
    We remove chemically this layer with fluoric acid or a plasma machine
    We iterate until we reach the lowest layer (metal 1)

## Slide 12: Reverse Engineering Reverse the Layout
We can the reconstitute the IC whole structure
This operation is very complex and time consuming
  In real life it is faster to focus on area of interest with a precise attack path
View of top métal
View of 1 metal lower after removal of top metals

## Slide 13: Reverse Engineering Read Memories Content
Extract (read) the not volatile memories content (data, code).
RAM, EEPROM, FLASH : difficult but possible
ROM:
  Easier
  Related to the kind of memory (diffused or not)
  Require different techniques
Depend to the technological node:
  90nm, 65nm
  28nm (!)
  7nm is the current best techno

## Slide 14: Read/Modify bits with Probing
Require a probe station

## Slide 15
We position one or more probes on a circuit area to ‘’read’’ or ‘’change/flip’’ a value (bits):
  For instance, the bit lines in a data bus, or code bus
  For instance, you can read a key value transferred on a bus to a memory or register
  You change the key bits ..
  Etc.
Read/Modify bits with Probing

## Slide 16: Modify the Circuit Focused Ion Beam (FIB)
FIB (Focused Ion Beam ) stations are most often used to analyze (and “debug”) failures in circuits
FIB can
  ‘’remove’’ metal, and modify connections
  He can add metal and then create new connections
Then an ATTACKER can
  Access to “hidden” signals at lower metal levels
  Modify the circuit (behavior)
Very expensive .. But low cost for renting !

## Slide 17: Modify the Circuit Focused Ion Beam (FIB)
Very powerful tool
Can defeat product security
Expensive
Can be rent
Usage to be be monitored
Cross Sections

## Slide 18: Countermeasures Vs. Invasive Attacks

## Slide 19: IC Reverse Engineering Countermeasures
Make design more complex
  Embed sensitive lines in lower levels
  Use thinner technologies (< 65 nm)
  Make the structure more compact (i.e.. Glue logic)
Glue Logic
  Makes the IP and block localization
  difficult to the attacker
IP easy to locate IP more difficult to locate

## Slide 20: Reverse Engineering on Memories Countermeasures
Use memory technology more difficult to reverse
Apply Scrambling / Permutations on data (addresses)
  Apply secret permutation to the data bits to make difficult the bit assembly once the memory has been reversed
  Can be software or hardware dedicated IPs
Hardware Data Encryption
  Data in memory are never in plain
  Encrypted with a cryptographic algorithm
  Must be very efficient as applied for each READ/WRITE access in memory
    Decryption for each memory read
    Encryption for each memory write
    Same for registers, etc.
  Difficult to design such algorithms (not a XOR with a hardcoded key please)
  Mandatory for serious products
Software Encryption
  Is recommended to be added at software level for (very) sensitive assets

## Slide 21: Probing Countermeasures
Passive Shield (insufficient)
  Full metal level on the top of the IC to “forbid” the access
Active Shield/Mesh (efficient)
  Full metal on top of the shield
  Embed active lines interconnected
  Touch or Cut a line and you will be detected by the shield sensors connected to the active lines
  https://hal.science/hal-00721569v2/document
Be a Clever Designer
  place sensitive buses, registers (data or configuration) in area difficult to access to a probe
Integrity Check on data flow
  Will detect a probe modification on data as integrity will not be coherent
Memories/Buses/Registers Encryption

## Slide 22: FIB Countermeasures
Active Shield/Mesh (efficient)
Full metal on top of the shield
Touch or Cut a line and you will be detected by the shield sensors connected to the active lines
Be a Clever Designer
place sensitive buses, registers (data or configuration) in area difficult to access to a probe
Difficult
With more and more efforts FIB can counterfeit most of the protection
Matter of time and money and techno used
Embed active lines interconnected

## Slide 23: 96’s: (well?)coming timing and side-channel attacks

## Slide 24: Timing Attack and Simple Power Analysis
1996 – P. Kocher first publication at Crypto conference
  Exploited timing analysis to recover the secret key used in RSA exponentiation thanks to several executions timing measurements
1998 – P. Kocher, B. Jaffe and Jun – SPA on RSA.
  Published on the CRI website.

## Slide 25: Some side-channel history
1999 – P. Kocher, J. Jaffe and B. Jun – first DPA publication on DES
  Paper: Differential Power Analysis. Crypto 1999.
1999 – T.S. Messerges, E.A. Dabbish and R.H Sloan – DPA on RSA
  Power Analysis of Modular Exponentiation in Smartcards. CHES 1999.
2000 – T.S Messerges – Second Order Power Analysis
  Using Second-Order Power Analysis to Attack DPA Resistant Software. CHES 2000.
2003 – E. Brier, C .Clavier and F. Olivier: CPA
  Correlation Power Analysis with a Leakage Model CHES 2004 (IACR 2003).
2008 – B. Gierlichs, L. Batina, P. Tuyls and B. Preneel: MIA
  Mutual Information Analysis. CHES 2008
2010 – A. Moradi, O. Mischke, and T. Eisenbarth: Collision Correlation on AES
    Correlation-Enhanced Power Analysis Collision Attack. CHES 2010

## Slide 26: What is this?

## Slide 27: What is this?
Zooming you identify loop of multiplications
 RSA exponentiation

## Slide 28: These ones?

## Slide 29: These ones?

## Slide 30: Triple DES

## Slide 31: Good AES Example Reading
From Francois Durvaux
SCA-Pitaya: A Practical and Affordable Side-Channel Attack Setup for Power Leakage–Based Evaluations
https://dl.acm.org/doi/fullHtml/10.1145/3371393

## Slide 32: Side-channel Leakage Origin
Devices are done using CMOS technology where the device power consumption varies depending on:
  The type of operation (code) executed
  The data manipulated by the hardware
Leakage models mostly considered in literature and practice
  Hamming weight: power consumption = F(data)
  Hamming distance: power consumption = F(reference_state XOR data)
  Single bit or multi-bit
  Direct value

## Slide 33: Remember RSA

## Slide 34: Implementing RSA (and ECC)
CRT RSA: modular exponentiation Md mod n is replaced by two exponentiations of half size.
As the complexity of this operation is in O(𝓵3) (with 𝓵 the bit-length of n) a half size exponentiation is 8 times faster.
The CRT-RSA is then theoretically about 4 times faster than the non-CRT exponentiation.
In practice, the efficiency gain will be closer to 3 than 4 due to the reduction and the recombination operations.
Most of the chip manufacturers include an arithmetic long integer accelerator, also said public key coprocessor, to compute modular multiplication operations more efficiently.
Depending on the manufacturer, the choice of the modular arithmetic can vary (i.e., Montgomery, Barrett, Quisquater).
It enables efficient implementations of RSA, CRT-RSA, DSA, DH schemes.
This coprocessor is also useful to implement efficient elliptic curves operations in ECDSA or ECDH schemes.

## Slide 35: Classical Exponentiation Square and Multiply
Left-to-right Square-and-Multiply Exponentiation
Right-to-Left Square-and-Multiply Exponentiation

## Slide 36: Modular Arithmetic Methods
The implementation of long integer efficient modular squaring and multiplication operations is of crucial importance for product makers.
Heavy constraints lie on these operations, especially in the context of embedded devices.
Several methods can be found in the literature. For instance, some common ones are the following:
  Montgomery method
  Barrett method
  Quisquater method
  Brickell method
  Sedlak method
  Scholar method (Knuth)
In practice the Montgomery and Barrett methods are the most efficient and most commonly used in most of the products.
Barrett, P. (1986). Implementing the Rivest Shamir and Adleman public key encryption algorithm on a standard digital signal processor. In Advances in Cryptology - CRYPTO '86, Santa Barbara, California, USA, 1986, Proceedings, pages 311-323.
Brickell, E. F. (1982). A fast modular multiplication algorithm with application to two key cryptography. In Advances in Cryptology: Proceedings of CRYPTO '82, Santa Barbara, California, USA, August 23-25, 1982, pages 51-60.
Knuth, D. E. (1997). The Art of Computer Programming, Volume 2 (3rd Ed.): Seminumerical Algorithms. Addison-Wesley Longman Publishing Co., Inc., Boston, MA, USA.
Montgomery, P. L. (1985). Modular multiplication without trial division. Mathematics of computation, 44(170):519-521.
Quisquater, J.-J. (1992). Encoding system according to the so-called RSA method, by means of a microcontroller and arrangement implementing this system. US Patent 5,166,978.
Sedlak, H. (1987). The RSA cryptography processor. In Advances in Cryptology - EUROCRYPT '87, Workshop on the Theory and Application of Cryptographic Techniques, Amsterdam, The Netherlands, April 13-15, 1987, Proceedings_, pages 95-105.

## Slide 37: Simple Side Channel Analysis

## Slide 38: Demo/TP on SSCA on RSA challenge
See demo on RSA SSTIC challenge 2019
Without clustering
With clustering
https://scikit-leaxrn.org/stable/modules/clustering.html

## Slide 39: Differential Side Channel Analysis

## Slide 40: Tools
Distinguisher
  Statistical tool used to compare simulated set (from guess) and real traces set (from DUT)
  DPA, CPA, SNR, NICV, MIA, ANOVA …
Discriminant:
  Function to apply to sort the distinguisher resulting scores
Model:
  Hamming weight, monobit, Hamming distance, value

## Slide 41: Differential Side-Channel Analysis
Run traces collection for cryptographic algorithm
Run EK (encryption) of N plaintexts P0 .. PN-1 store related side-channel traces C0 .. CN-1.
…
C0 = EK(P0) CN-1 = EK(PN-1)

## Slide 42: Side-Channel Analysis
Plaintext0
Ciphertext0
Plaintext1
Ciphertext1
Plaintext2
Ciphertext2
Plaintext3
Ciphertext3
PlaintextN-1
CiphertextN-1

## Slide 43: Differential Side-Channel Analysis
Apply Divide-and-Conquer method on the operations and involved key-bits
  Guess 𝛌 bit of key chunk: for instance, 6-bit for TDES SBoxes, 8-bit for AES ByteSub
  Break down the problem = full key recovery to sub-problem = recover key per bit-chunk involved in sub operations
  Define the computation targeted
  Selection function = KeyAddition Substitution …. In first or last rounds

## Slide 44: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
P0
P1
P14
P15
…
K0
K1
K14
K15
…
⊕
Guess 0
256
n plaintexts
Guess 1
Guess 255
Selection function output K0

## Slide 45: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
1C
P1
P14
P15
…
00
K1
K14
K15
…
⊕
0x1C
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext 0

## Slide 46: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
8A
P1
P14
P15
…
00
K1
K14
K15
…
⊕
0x1C
0x8A
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext 1

## Slide 47: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
73
P1
P14
P15
…
00
K1
K14
K15
…
⊕
0x1C
0x8A
0x73
…
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext n-1

## Slide 48: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
AB
P1
P14
P15
…
01
K1
K14
K15
…
⊕
0xAB
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext 0
0x1C
0x8A
0x73
…
…

## Slide 49: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
12
P1
P14
P15
…
01
K1
K14
K15
…
⊕
0xAB
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext 1
0x1C
0x8A
0x73
…
…
0x12

## Slide 50: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
F1
P1
P14
P15
…
01
K1
K14
K15
…
⊕
0xAB
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext n-1
0x1C
0x8A
0x73
…
…
0x12
0xF1
…

## Slide 51: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
87
P1
P14
P15
…
FF
K1
K14
K15
…
⊕
0xAB
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext n-1
0x1C
0x8A
0x73
…
…
0x12
0xF1
…
0x87
0x23
0x9D
…

## Slide 52: Selection Function
256 × n
Key byte 15
Guess 0
256
n plaintexts
Guess 1
Guess 255
…
256 × n
Key byte 0
16

## Slide 53: Now use a distinguisher …
Guess 0
n plaintexts
…
…
…
…
Guess 1
Guess 255
256
Simulated Data from guesses
Measurement Data
n traces

## Slide 54: Differential Side-Channel Analysis DPA for Differential Power Analysis
Guess 0
n plaintexts
…
…
…
…
Guess 1
Guess 255
256
0x1C
Model
MonobitMsb(0)
Partitioning
0
Set G0
Set G1

## Slide 55: Differential Side-Channel Analysis DPA for Differential Power Analysis
Guess 0
n plaintexts
…
…
…
…
Guess 1
Guess 255
256
0x1C
Model
MonobitMsb(0)
Partitioning
1
…
Set G0
…
Set G1
0x8A

## Slide 56: Differential Side-Channel Analysis DPA for Differential Power Analysis
Guess 0
n plaintexts
…
…
…
…
Guess 1
Guess 255
256
0x1C
Model
MonobitMsb(0)
Partitioning
0
…
Set G0
…
Set G1
0x8A
0x73

## Slide 57: Differential Side-Channel Analysis DPA for Differential Power Analysis
Bit 0 Set
Bit 1 Set

## Slide 58: Side-Channel Analysis
Bit 0 Set
Bit 1 Set
Average traces

## Slide 59: Side-Channel Analysis
Wrong assumption
Good assumption
,
,

## Slide 60: Differential Side-Channel Analysis Not always efficient technique
Correct Guess
Wrong Guess
Here DPA is not efficient with this number of traces !!!
HOW CAN WE IMPROVE?

## Slide 61: Correlation Side Channel Analysis The first break event since 1998.

## Slide 62: Correlation Power Analysis
Bravais-Pearson Correlation Factor can be used to measure the statistical dependency between two set of data
  Linear Regression
Remember we have the following two sets: we want to evaluate if they are “closed”
Measurement Data
Simulated Data from guesses

## Slide 63: Correlation Power Analysis
Two variables (data sets) are linearly related
 the correlation coefficient will be high
If the two data sets are not linearly related
 the correlation coefficient will be low.
Most cases have shown Linear leakage model in Hamming weight is efficient
Model:
  W = a × HW(data) + b + noise

## Slide 64: Correlation Power Analysis

## Slide 65: Now use Correlation Analysis
Guess 0
n plaintexts
…
…
…
…
Guess 1
Guess 255
256
Simulated Data from guesses
Measurement Data
n traces

## Slide 66: Now use Correlation Analysis
Guess 0
n plaintexts
W0
…
Guess 1
Guess 255
256
Correlation
(W0 , C)
C

## Slide 67: Now use Correlation Analysis
W1
Guess 0
n plaintexts
…
Guess 1
Guess 255
256
Correlation
(W1 , C)
C

## Slide 68: Now use Correlation Analysis
WK
Guess 0
n plaintexts
…
Guess 1
Guess 255
256
Correlation
(WK , C)
C

## Slide 69: Now use Correlation Analysis
W255
Guess 0
n plaintexts
…
Guess 1
Guess 255
256
Correlation
(W255 , C)
C

## Slide 70: Correlation Attack Result

## Slide 71: Correlation Power Analysis
We can use information from all bits contrarily to DPA – no information loss
  All operand and values can be used with
    Mono-bit attacks
    Hamming weight attack
    Value itself to be correlated
This model is linear in the HW or HD
  But it is close to the real behaviour of a circuit
  Indeed, the Hamming measures the number of bit flips entre between a state i and the next state i+1
    Example: writing in a register R0
      R0 = a
      R0  R0  K
      R0 = b Bit flip a  b  K
Requires about 10 times less traces than DPA; no “ghost” peaks

## Slide 72: CPA demonstrations on DES and AES
DPA vs CPA on XMEGA AES Traces
DSCA on DES DPA contest V1
DSCA on AES DPA contest V2

## Slide 73: Categories of Countermeasures
Desynchronize
  Hardware de-synchronization: jitter, clock and frequency jitters, random delays
  Shuffling
  One amongst N techniques
Protocol
  Paddings
  Session keys,
  Fresh re-keying
  Unknown input and/or output (partially): CTR mode, payment ATC
De-correlate
  Hardware techniques to balance consumption (dual rail)
  Masking techniques

## Slide 74: One among N countermeasure(s)
…
AES
AES
AES
AES
DES
DES
AES
…
…
AES
AES
AES
AES
AES
AES
AES
…
…
AES
AES
DES
DES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
AES
…
…

## Slide 75: One among N countermeasure(s)
Same input message with fake keys
Different (random fake input) messages for correct key: key is manipulated more (!!)
…
AES
AES
AES
AES
DES
DES
AES
…
…
AES
AES
AES
AES
AES
AES
AES
…
…
AES
AES
DES
DES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
AES
…
…

## Slide 76: Attacking: one among N countermeasure(s)?
Same input message with random fake keys
What attack do you recommend?
  Ghost peaks?
…
AES
AES
AES
AES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
AES
…
…

## Slide 77: Attacking one among N countermeasure(s)?
Same input message with random fake keys
What attack do you recommend? Ghost peaks?
Cipher texts attacks are more efficient
…
AES
AES
AES
AES
DES
DES
AES
…
…
AES
AES
AES
AES
AES
AES
AES
…
…
AES
AES
DES
DES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
…
…
AES
AES
AES
AES
AES
AES
AES
…
…

## Slide 78: Masking Techniques
Data Masking with random values
  The idea
    Ai  K = Bi can be attacked with DPA..
    Use a random X and replace by
      Ai  X = Ci
      Ci  K = Di
      Di  …  Ei
      Ei  X = Bi
  The bit-flips and IC power consumption changes at each execution
Several countermeasures based on this principle published
Can be Boolean (TDES, AES) and/or arithmetic masking (HMAC)

## Slide 79: AES first operations
SuBbytes
P0
P1
P14
P15
…
A0
A1
A14
A15
…
K0
K1
K14
K15
…
⊕

## Slide 80: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
P0
P1
P14
P15
…
K0
K1
K14
K15
…
⊕
Guess 0
256
n plaintexts
Guess 1
Guess 255
Selection function output K0

## Slide 81: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
1C
P1
P14
P15
…
00
K1
K14
K15
…
⊕
0x1C
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext 0

## Slide 82: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
8A
P1
P14
P15
…
00
K1
K14
K15
…
⊕
0x1C
0x8A
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext 1

## Slide 83: Selection Function Key Byte 0
SuBbytes
P0
P1
P14
P15
…
73
P1
P14
P15
…
00
K1
K14
K15
…
⊕
0x1C
0x8A
0x73
…
Guess 0
256
n plaintexts
Guess 1
Guess 255
Plaintext n-1

## Slide 84: AES
SubBytes
P0
P1
P14
P15
…
A0
A1
…
K0
K1
K14
K15
…
⊕
A14
A15

## Slide 85: AES side-channel masking
SubBytes
P0
P1
P14
P15
…
A0 ⊕ ?
A1⊕ ?
…
K0
K1
K14
K15
…
⊕
Select random mask R
SR, MixColumn are linear, easy to mask and unmask
  F(A ⊕ R ) = F(A) ⊕ F(R)
SubBytes is not linear, more complex operation
  SubBytes(A ⊕ R ) ≠ SubBytes(A) ⊕ SubBytes(R)
⊕
R
R
R
R
…
A14⊕ ?
A15⊕ ?
How to protect the SubBytes ?

## Slide 86: AES side channel masking
SuBbytes*
P0
P1
P14
P15
…
K0
K1
K14
K15
…
⊕
for value from 0 to 255
  SubByte_Masked [value ⊕R] = SubByte[value ] ⊕ R
ShiftRow
MixColumn
A0 ⊕ R
A1⊕ R
…
A14⊕ R
A15⊕ R
B0 ⊕ R
B1⊕ R
…
B14⊕ R
B15⊕ R
⊕
R
R
R
R
…
Repeat on all Rounds
…
 then unmask!

## Slide 87: More …
Can be done similarly on T table implementation of AES
Bigger tables require more memory
Faster

## Slide 88: High Order Side-Channel Analysis

## Slide 89: Second (Higher) Order Attacks
Find two instants on the trace where:
i1: the mask R is manipulated
I2: target data D masked with R is manipulated
i1 : R
i2 : D ⊕ R
R ⊕ (D ⊕ R) = D
HW(R) ⊕ HW(D ⊕ R) ≠ HW(D)
HW(R) ⊕ HW(D ⊕ R) ≈ HW(D)

## Slide 90: Reminder on Second order attacks
2nd Order Attack Principle:
  Find two instants i1 and i2 on the trace(s) where the mask R is manipulated
  Combine those two instants i1 and i2 to remove the mask influence
  Perform classical 1st order attack
Method 1: Combine i1 and i2 with Absolute Difference :
  T* = abs(i1 – i2)
  Correlation (T*, guesses)
Method 2: Combine i1 and i2 with Normalised (Centered) Product
  E1 the mean of i1 and E2 the mean of i2
  T* = (i1 - E1)*(i2 - E2)
  Correlate (T*, selection_function_values)

## Slide 91: More second order attacks
Can be difficult to locate R
Combine SubBytes(P0⊕R) with SubBytes(P1⊕R)
  Requires 216 guesses instead of 28
Combine Round-1- SubBytes(P0⊕R) with Round-10-SubBytes(P0⊕R)
  Requires 216 guesses instead of 28
…

## Slide 92: Second Order Attack Demonstration
See notebook demonstration on second order attack.

## Slide 93: How to improve resistance
Diversify the masks
  One random mask per byte on linear operations
  Change mask at each round
  Easy to handle for ShiftRow and MixColumn
One random byte per SubByte operation in the round
  Requires 16 masked new SubBytes
Add Shuffling: random order execution
  Mainly on SubBytes operations
Add one AES among N countermeasure
Implement SubBytes differently
  Can perform inversion in GF(16) instead of GF(256)
  Smaller table, more masks, more permutations
Implement the inversion in GF(256) and mask the operation with a combination of multiplicative (additive and Boolean masking)
It will make the second order attack theoretically possible but more complex to perform in practice

## Slide 94: Obscurity
Not Kerckhoffs’s principle:
  “A cryptosystem should be secure even if everything about the system, except the key, is public knowledge.”
Shannon
  ”one ought to design systems under the assumption that the enemy will immediately gain full familiarity with them”
Can help against side-channel if added on top of standard crypto algorithm
Not a countermeasure “recommended”
AES
P
H
Key K

## Slide 95: Infective Computation
Add integrity or MAC
If not correct execute but with fake key instead of correct one
Make the attacker losing time on fake data
Attacker must not detect the key is fake (you detected him)

## Slide 96: Multiplicative Masking Technique
Several countermeasures (publication) involve multiplicative masking
    Boolean mask is now multiplicative
    Inversion gives:
Not sensitive to high order attacks
Sensitive to ZERO VALUE attacks

## Slide 97: dth order resistant implementations
Split the data D and key K to be protected into d+1 random shares to prevent the product from dth high order side-channel attacks.
The principle is the following:
  Generate d random values r1, …, rd
  Generate d random values k1, …, kd
  Compute r0 = D  r1  … rd
  Compute s0 = K  s1  … sd
D  K = (r0  s0)  (r1  s1)  …  (rd  sd)

## Slide 98: dth order resistant implementations
ISW (Ishai – Sahai – Wager) scheme
  Y. Ishai, A. Sahai, and D. Wagner. Private Circuits: Securing Hardware against Probing Attacks. In D. Boneh, editor, Advances in Cryptology – CRYPTO 2003,
  AND and NOT gates circuit
M. Rivain and E. Prouff
  Provably Secure Higher-Order Masking of AES. CHES 2010
L. Goubin and A. Martinelli
  Protecting AES with Shamir’s Secret Sharing Scheme. CHES 2011.

## Slide 99: Fresh Rekeying
Provide side-channel resistance by
  limiting the side-channel attacks paths as different keys are used in the computations.
  Re-Keying can be done externally via the protocol or internally.
  We focus here on internal Re-Keying.
designing a function g to re-key a block cipher f
  with a master and constant values with a random nonce r.
  Then each encryption of a plaintext block is performed with a fresh key k*
  such that the ciphertext is c = fk*(p).
  It can also be decided to relax the model and to use a fresh key
    for a given number w of plaintext blocks encryptions
    ensuring the number L is small enough to prevent the TOE from profiled and not profiled attacks.
Make use of functions more resistant to side-channel than others …

## Slide 100: Tree Key

## Slide 101: Real Example in Secure Boot

## Slide 102: Back to RSA

## Slide 103: How to protect RSA from SSCA .. Use an atomic exponentiation
Squaring and multiplication are done using the same operation Multiply Always exponentiation
Previous simple analysis is not efficient anymore.

## Slide 104: … Or with Regular Implementations

## Slide 105: … Not enough to prevent DSCA …
See demo notebook for DSCA on Exponentiation

## Slide 106: Blinding
Multiplicative message blinding
M* = re mod N r a large random value, e the public exponent
Additive message blinding
M* = M + r1.N mod r2.N r1, r2 large random values

## Slide 107: There are still possible attacks
Cross Correlation
Distinguishing Squaring from Multiplying operations
The Doubling (Squaring) Attack

## Slide 108: Add the exponent blinding countermeasure
Euclidean division exponent blinding
d = r.d1 + d2 r a large random value > 128 bits
 Md = (Mr)d1 × Md2 mod N
Additive exponent blinding
d* = d + r.𝛗(N) r a large random value > 128 bits, 𝛗 the Euler function
Exponent split
d1 = d – r r a large random value > 128 bits
 Md = Md1 × Mr mod N

## Slide 109: Combining Several Countermeasures
Example combining:
Atomic exponentiation
Additive message blinding
Additive exponent blinding

## Slide 110: Single Trace Attack on blinded RSA with Clustering techniques
See demo on RSA SMA
With clustering
https://scikit-leaxrn.org/stable/modules/clustering.html

## Slide 111: Side-Channel Methodology

## Slide 112: Side Channel Methodology
Tests Plan
Observe
Collect
Align
Characterize
Attack
Analyse and decide
Measure

## Slide 113: Side Channel Attacks Methodology Step 1: Tests Plan
Evaluation mode
  Knowledge on the product is given for the evaluation
  Source code, IC design, cryptographic operations and IPs, etc.
  information given
Vulnerability Analysis
  Identify potential attack if information available
Test Plan
  Define tests based on Vulnerability Analysis if it was performed.

## Slide 114: Side Channel Attacks Methodology Step 2: Measurement
Measurement set-up
  Setup the measurement
    Select probe, location
    Sampling rate,
    EM (preferably often)
    Triggering
  Identify the operation you are targeting
  Find the best signal for the operation
  targeted,
Cartography can help

## Slide 115: Side Channel Attacks Methodology Step 3: Locate / Process with Few traces Observation
What is the knowledge you can get to locate and identify?
Observe the trace
  What can you identify?
  Seeing the algorithm rounds? rounds operation?
Chosen input
  Depending on the leakage model of the device for the targeted operation, fixing a certain number of bytes to a constant (i.e., 0) can make appear specific patterns in the trace to locate the interesting area in the trace or even to recover secret.
Signal Processing
  Apply signal processing techniques to observe potential loops, identify better the operations related to the computations
  Investigate better signal processing that will be helpful for aligning the traces once collected

## Slide 116: Side Channel Attacks Methodology Step 4: Collect traces
Define setup
  Sampling to use
  Define Area to collect in the computation for the chosen attack path
  (first or last rounds for example)
  Setup for trace collection
Run the traces collection
  Collect traces and store
  100K? 1M? 10M?
  Efficient equipment required (up to 1M per day)

## Slide 117: Side Channel Attacks Methodology Step 5: Align
Alignment
  Identify which signal processing techniques to combine to align traces
  Run the alignment(s)
Critical Path
  Alignment can determine the success or failure of the attacks
  Major part of the global effort

## Slide 118: Example: observe then align
See observation notebook on aligned and not aligned traces

## Slide 119: Side Channel Attacks Methodology Step 5: Characterize
What is the knowledge you can get to characterize?
Input – Output
  Knowing the computation input and/or output (plaintext or ciphertext) can help
  Perform SCA tests on input to locate the beginning of the targeted operation in the trace(s)
  Perform SCA tests on output to locate the end of the targeted operation in the trace(s)
  Require a first traces collection to be done
Chosen input  TVLA Test Vector Leakage Assessment i.e., T-test …
  You can select specific values as input to get more knowledge on the operations and find leakages points, T test
  Fixing a certain number of bytes to a constant (i.e., 0) can reduce the algorithmic noise from one operation on the targeted one
  Depending on the leakage model of the device for the targeted operation, fixing a certain number of bytes to a constant (i.e. 0) can make appear specific patterns in the trace to locate the interesting area in the trace or even to recover secret.

## Slide 120: Side Channel Attacks Methodology Step 6: Characterize
What is the knowledge you can get to characterize?
Key Knowledge  Leakage Detection on Data Computation with Key Knowledge
  Knowing the key means you can characterize your implementation (at each step, each round)
    You can test to correlate each intermediate value of the computation with the trace
    Answer: YES there is leakage in the implementation  might lead to an attack exploitation
    Answer: NO there is no obvious leakage in the implementation
Chosen Key Leakage Detection on Key Manipulation with Key Knowledge
  Knowing the key allows to characterize the key schedule (T-test, reverse with varying keys)
  Can be used to build templates on the key manipulation
Characterization results provide first test conclusion.

## Slide 121: Side Channel Attacks Methodology Step 7: Attack
Run the attacks
Test different leakages models
Test all selection functions
Log results
Observe results
Can use thresholds to sort the result at a first stage
  score value higher to a threshold
  Ratio between best score and next higher ones.
No characterization knowledge
Use characterization results to run appropriate attacks
Tests related attack paths
  (model, selection functions..)
Log results
Observe results coherency with characterization
With characterization knowledge

## Slide 122: Side Channel Attacks Methodology Step 8: Analyse and Decide
Conclude on testing and evaluation
Or relaunch different tests if there is a plan.

## Slide 123: Welsch t-test
Most used test is the student T-test
Requires the evaluator can send chosen messages
  Using random and fix plaintext sets
  Variance based test
  Identify 1st order leakages
Can be turned to higher order leakages detection

## Slide 124: TVLA and t test
The initial publication dealing with using the Welch's t test for TVLA is the following one in 2008:
https://csrc.nist.gov/csrc/media/events/non-invasive-attack-testing-workshop/documents/08_goodwill.pdf

## Slide 125: Welsch t test
T-test examines the leakage of the Device Under Test (DUT) independent of its underlying architecture.
Gives a level of confidence to conclude that the DUT has an exploitable leakage or not.
However, it provides no information
  about the easiness/hardness of an attack which can exploit the leakage,
  nor about an appropriate intermediate value and the hypothetical model.
Can easily and rapidly report that the DUT fails to provide the desired security level:
  e.g., due to a mistake in the design engineering
  or a flaw in the countermeasure.
T-test analysis requires to acquire at least two (better more) sets of traces:
  Set A provides random data
  Set B provides fix or semi-fix data
  The targeted data could be any of the algorithm inputs (plaintext, key, mask ...).
[GJJR] G. Goodwill, B. Jun, J. Jaffe, P. Rohatji - A testing methodology for side-channel resistance validation. https://csrc.nist.gov/csrc/media/events/non-invasive-attack-testing-workshop/documents/08_goodwill.pdf
[SM15] Tobias Schneider and Amir Moradi. Leakage Assessment Methodology - a clear roadmap for side-channel evaluations. CHES-2015 - https://eprint.iacr.org/2015/207.pdf
[BCDJKKLMRS] G. Becker, J. Cooper, E. DeMulder, G. Goodwill, J. Jaffe, G. Kenworthy, T. Kouzminov, A. Leiserson, M. Marson, P.Rohatgi and S. Saa. Test Vector Leakage Assessment (TVLA) methodology in practice

## Slide 126: t test

## Slide 127: TP of t-test on AES
See demo/TP notebook on AES

## Slide 128: Attack and Remaining Key Entropy
How to evaluate the results of a side-channel attack
  Do we really need the full key to be recovered?
  Remaining entropy is the right cursor !
  https://eprint.iacr.org/2014/920.pdf

## Slide 129: Cryptographic Protocol vs.. Cryptographic Algorithm … Sometimes there is still space somewhere around the algorithm for something different

## Slide 130: Side-Channel Attack on the MAC Algo3 2015 (only…)
Developers MUST prevent their product from side-channel attacks
  First and higher order(s)
  Cryptographic engineers develop strong DES and AES
These algorithms are used in protocols
  Weakness can be in the protocol
  MAC Algo3 is an ISO protocol
    DES CBC chaining mode
    End with a TDES operation

## Slide 131: MAC Algo3

## Slide 132: MAC Algo3

## Slide 133: Side-Channel Attack on MAC Algo3
Set P1 to constant, i.e. 0
Execute MA3
  with random values for P2: P2,0 to P2,n
  Collect execution traces C0 … Cn
Perform CPA on P2 xor C1
  C1 = DES(0, K1)
Recover the value C1
Brute force C1 and recover K1
Brute force MAC and recover K2.

## Slide 134: Attack Result

## Slide 135: Today? More and more side-channel attacks in real life.

## Slide 136
Side-channel
Target any Kind of Integrated Circuit
Smartcards, Secure Elements, FPGA, SoC FPGA, complex SoC in mobiles, computers …
Nvidia Tegra 2 SoC

## Slide 137: Wide Range of Products Nowadays
Smart cards: contact, contactless or dual interface
RFID Tags
Tokens, USB keys, SSD secure storage
Set-top-Box
FPGAs
Systems on Chips (SoC)
Mobile Phone
Military Products

## Slide 138: Attack categories
Measurement: power, RF, EM
Timings Attacks
Simple Side-Channel Analysis
Differential Side-Channel Analysis
Advanced Side-Channel Attacks:
  Horizontal,
  High Order
Profiled vs. Not Profiled Attacks
  Template Attacks
  Deep Learning
Example of side-channel attack classification proposed in:
Systematic Classification of Side-Channel Attacks: A Case Study for Mobile Devices Raphael Spreitzer, Veelasha Moonsamy, Thomas Korak, and Stefan Mangard

## Slide 139: Open Sources
Lascar https://donjon.ledger.com/about/
Scared https://github.com/eshard/scared
Side-Channel marvels: https://github.com/SideChannelMarvels
REASSURE project https://reassure.eu
SCALib https://github.com/simple-crypto/SCALib
Languages:
  From C, C++, Matlab, Maple
  to Python, Numpy, Scipy, Jupyter Lab, Julia, Sage

## Slide 140: A side journey to Titan
https://ninjalab.io/a-side-journey-to-titan

## Slide 141: 2024: EUCLEAK

## Slide 142
ECDSA secret key recovery from partial scalar leakage
From full scalar k recovery the secret key d can be recovered with:
It might happen only few bits of k are recovered: d can not be recovered with this formula.
It is still possible when several consecutive bits of the scalar are recovered for several ECDSA signatures to recover d using lattices reduction.
See papers below.
Fig. from [Poussier et al.]

## Slide 143: SideLine attacks
https://eprint.iacr.org/2020/1127.pdf
REMOTE side channel attack on device !
And also now remote fault attack on devices.

## Slide 144: Post Quantum Cryptography

## Slide 145
https://quantumpedia.uk/a-brief-history-of-quantum-computing-e0bbd05893d0

## Slide 146: (Pre-Quantum) Cryptography : TODAY
Cryptography | Algorithms | Strength
Symmetric | AES-128 /AES-192 / AES-256 AES-GCM Chacha20 HMAC-SHA-256. Poly1305 SHA-2 / SHA-3 / Salsa20 | 2128 to 2256
Asymmetric | RSA / DSA 2048-4096 ECDH / ECDSA P-256 / P-521 ECIES - EdDSA | 2128 to 2256

## Slide 147: Schor’s algorithm
1994 Schor designed quantum algorithm
Capable to solve big integer factorization and discrete logarithm resolution mathematical problem in polynomial time compared to GNFS that is sub-exponential time.
RSA, DH, DSA, ECDH, ECDSA security defeated when quantum computers with sufficient qubits allows Schor’s algorithm execution.

## Slide 148: Grover’s algorithm
1996 Grover designed quantum algorithm to speed up symmetric cryptography algorithm key recovery
Offering a quadratic speedup compared to classical algorithms, which require approximately N steps.
Grover’s algorithm is less dramatic than that of Shor’s algorithm, it still demonstrates the potential of quantum computing to outperform classical computing in specific tasks..

## Slide 149: Quantum Computer is coming … Quantum Computer is there?

## Slide 150: Quantum Computer is coming … Quantum Computer is there?

## Slide 152
?CHAOS

## Slide 153: (Pre-Quantum) Cryptography : TODAY
Cryptography | Algorithms | Strength
Symmetric | AES-128 /AES-192 / AES-256 AES-GCM Chacha20 HMAC-SHA-256. Poly1305 SHA-2 / SHA-3 / Salsa20 | 2128 to 2256
Asymmetric | RSA / DSA 2048-4096 ECDH / ECDSA P-256 / P-521 ECIES - EdDSA | 2128 to 2256

## Slide 154: Cryptography with Quantum Computers
Cryptography | Algorithms | Strength
Symmetric | AES-128 /AES-192 / AES-256 AES-GCM Chacha20 HMAC-SHA-256. Poly1305 SHA-2 / SHA-3 / Salsa20 | 2128 to 2256128
Asymmetric | RSA / DSA 2048-4096 ECDH / ECDSA P-256 / P-521 ECIES - EdDSA | 2128 to 2256 0

## Slide 155: Cryptography with Quantum Computers
Cryptography | Algorithms | Strength
Symmetric | AES-128 /AES-192 / AES-256 AES-GCM Chacha20 HMAC-SHA-256. Poly1305 SHA-2 / SHA-3 / Salsa20 | 2128 to 2256128
Asymmetric | RSA / DSA 2048-4096 ECDH / ECDSA P-256 / P-521 ECIES - EdDSA | 2128 to 2256 0
NEED FOR NEW POST QUANTUM RESISTANT ALGORITHMS FOR ASYMMETRIC CRYPTOGRAPHY

## Slide 156: Post Quantum Cryptography Timeline

## Slide 157: Post Quantum Cryptography Timeline

## Slide 158: Post Quantum Cryptography

## Slide 159: Post Quantum Cryptographic Selected Algorithms
https://csrc.nist.gov/Projects/post-quantum-cryptography/selected-algorithms-2022

## Slide 160: 2023 2025
Industry is performing R&D to implement and secure PQC
  Hardware coprocessor for NTT
Challenge on hardware resources: RAM – execution time – KEY STORAGE
Implement side-channel countermeasures
TO COMPARE with
  512 bytes for key length and signature size with RSA-4096

## Slide 161: Conclusion on PQC

## Slide 162: Attack Potential and JIL Rating

## Slide 163: Attack Factors
For each step, the evaluator considers 6 factors according to the CEM:
  Amount of time
  Level of expertise
  Level of knowledge of the TOE
  Level of opportunity
  Equipment required
  Open Sample required or not
For each factor a value is provided in a table
The attack potential is the sum of all values
Factors | Identification | Exploitation
Elapse time |  | 
Expertise |  | 
Knowledge of the TOE |  | 
Access to the TOE |  | 
Open Sample |  | 
Equipment |  | 
Sub-total |  | 
TOTAL |  | 

## Slide 164: Elapsed Time
Two steps are considered: preparation and realization…

## Slide 165: Expertise definition
Expertise also depends on the tools required to perform the attack: Optical Microscope, Chemistry (etching, grinding), Micro-probing station, Laser Cutter, Radiation, Plasma (etching, grinding), Focused Ion Beam (FIB), Scanning Electron Microscope, (SEM), Scanning Force Microscope (SFM)

## Slide 166: Expertise Rating
If several experts are required for the same domain, the highest expertise level is considered for each step
The level “Multiple Experts” is designed for applicable when several experts of different domains are required (e.g. hardware and crypto)

## Slide 167: Knowledge of the TOE
The knowledge of the TOE can be gained through unclassified or unprotected information, or collusion with a developer.
The following classification is to be used:
  Public: information in the public domain,
  Restricted: information from development (specifications, guidance)
  Sensitive: HLD and LLD information.
  Critical: Implementation representation (Design and Source Code).
  Very Critical: Data requiring also heavy specific tools
Information discovered by Reverse Engineering will be rated as Id step…

## Slide 168: Access to the TOE
Availability of samples (in terms of time and cost) and number of samples needed to succeed
Reasons to need more than one sample:
  the attack succeeds only with some probability,
  The attacker needs to collect information from several copies of the TOE.

## Slide 169: Equipment
Equipment category considers price and availability:
  Standard
  Specialized (expensive equipment found in universities)
  Bespoke: very expensive or difficult to keep confidential
  Multiple Bespoke: several different bespoke equipment
A value is given for all equipment used in IC business but this must always be reevaluated with technical progress…

## Slide 170: Access to Open Samples
When the evaluator attack uses « open samples » or classified information, this « advantage » is considered in the rating…
This Open Sample rating sometimes replaces the discovery step, and may give a lower result

## Slide 171: Rating the Attack
Sum the values for each factor, in preparation and exploitation, for each successful attack
Compute the rating for both paths with / without access to open samples, and keep the lowest
The lowest rating gives the resistance of the TOE

## Slide 172: Final Table

## Slide 173: Rating Example with a CEMA on AES
AES in a secure element
CEMA successful.
The product is resistant to an Enhanced Basic potential attack:VAN.3
In that case certification is a FAIL as AVA VAN.5 was the mandatory requirement.
Factors | Identification | Exploitation
Elapse time | 2 (< 1 week) | 3 (< 1 day)
Expertise | 5 (expert) | 2 (Proficient)
Knowledge of the TOE | 2 (restricted) | 0 (public)
Access to the TOE | 0 (<10 samples) | 0 (<10 samples)
Open Sample | 0 | 0
Equipment | 3 (specialized) | 4 (specialized)
Sub-total | 12 | 9
TOTAL | 21 | 

## Slide 174: Questions?

## Slide 175: THANKS

## Slide 176
Find out more at www.st.com
You can personalize this
last page with a short link
(ex. www.st.com/shortlink)
You can find a complete list of st.com short links on this page:
http://seo.st.com/toolbox/shortcuts/

## Slide 177
For further support in creating a PowerPoint presentation, including graphic assets, formatting tools and additional information on the ST brand
you can visit the ST Brand Portal https://brandportal.st.com
Please remove this page
before publishing the
presentation